## Slide 1: OpenAMP: Virt I/O MMIO w/ MSI
Joshua Pincus
October 27, 2020

## Slide 2: Agenda
Goals
Background
Current Research Focus
Status Update
Results
Demo

## Slide 3: Goals
Objective: Migrate to an emulation-free environment with Virt I/O (MMIO transport)
Step 1: Statically define configuration details
  Memory for queues and shared data structures is allocated in advance via shared memory
  Features are communicated without negotiation
  Interrupts and related resources are defined in advance
Step 2: Improve interrupt latency via MSI
Step 3: Send events without emulation using hardware resources
Step 4: Demonstrate Virt I/O devices running on new framework

## Slide 4: Background
Virt I/O MMIO performance is below par
  One legacy interrupt for all queues
  Interrupt acknowledgement involves several emulated operations
    Check status
    ACK interrupt
  Notification of events also requires several emulated operations
    Select a queue
    Trigger an event via NOTIFY
    All queue events are multiplexed through one NOTIFY
Virt I/O on X86 can use PCI or MMIO.
Virt I/O on ARM (mostly) relies on MMIO.

## Slide 5: Current Research Focus
Intel developed an MMIO + MSI prototype
  Public patches for Linux virt I/O MMIO driver
  Public patches to the 1.1 Virt I/O specification
  QEMU and LKVM changes are left as an exercise to the wary developer
Two sets of changes are included in the proposed spec update:
  MSI support
    Share vectors among queues: Map vectors to queues dynamically
    Not share vectors among queues: Vectors and queues share a 1:1 relationship
    MSI configuration and commands available to caller (mask, unmask, etc.)
  MSI notification support
    Writes to specific regions of memory trigger events specific to a queue
    Implemented as an array indexed by vector

## Slide 6: Status Update
Linux changes and proposed spec were reversed to figure out what the emulation framework (aka LKVM) required.
LKVM’s Virt I/O MMIO implementation was augmented by borrowing heavily from the Virt I/O PCI MSIX implementation.
MSI sharing/non-sharing were both implemented.
MSI notification was also implemented.
  Still relies on emulation to function but shows cost of using ‘notify’ register
  May be adapted to be hardware-specific, aka a write to the LAPIC/IOAPIC or GIC/ITS instead of writing to an emulated register
Linux YOCTO environment w/ UBUNTU used to warrant LKVM

## Slide 7: Results: Performance
Test | Virt I/O PCI | Virt I/O MMIO w/o MSI | Virt I/O MMIO w/ MSI
TCP_RR (host -> guest) | 20182 | 11009 | 20352
TCP_RR (guest -> host) | 20463 | 10955 | 20058
TCP_RR measures round trip latency (more trans/s = lower latency)
Host is a Walnut Canyon system with Ubuntu
Guest is Yocto Linux running via LKVM

## Slide 8: Results: Emulation Traps
 | TRAP (R) | TRAP (W) | CHECK IRQ (R) | ACK IRQ (W) | NOTIFY(W) | IRQ (host signal) | MSI (host signal)
Virt I/O MMIO w/o MSI | 652633 | 652638 | 652615 | 652615 | 329666 | 660911 | 0
Virt I/O MMIO w/ MSI | 20 | 66 | 0 | 0 | 591161 | 0 | 1.182M
IRQ: 1M more traps => 600K fewer interrupts handled
MSI: 2x the number of interrupts => 80%+ improved transfer rate

## Slide 9: Demo
Use LKVM to present a virtio-mmio instance of the virt I/O network device to an x86_64 YOCTO guest
LKVM w/o MSI
  Show legacy interrupt settings
  Demonstrate netperf transmit rate via TCP_RR request/receive test
LKVM with MSI
  Show that MSI interrupts are being allocated
  Demonstrate netperf transmit rate via TCP_RR request/receive test

## Slide 10: Next Steps
Modify LKVM tool to accommodate both Linux and VxWorks guests
Test other Linux device drivers against LKVM changes
Test MMIO + MSI changes on ARM target (Xilinx, Rasp Pi)
Refine the Intel patches
  Refine spec changes
  Submit spec and code changes to Intel contacts for discussion + approval
Discuss performance improvements with Virt I/O community
Update LKVM to handle Virt I/O 1.1+ (Only legacy spec is supported)

## Slide 11
™
11
© 2018 WIND RIVER. ALL RIGHTS RESERVED.